## Slide 1: The MegaDerm 3000
Team 9
Kristen Hagan
Mahy Hussain
Laura Kenyon
Thomas Leahy

## Slide 2: Process Overview

## Slide 3
Perform single-image Analysis on every image
Process Overview
Prompt user to input image stack
Prompt user to crop the ruler and mole
Find the pixel/mm conversion factor
Detect the
lesion border
Calculate lesion
area
Calculate asymmetry coefficients
Calculate Color
Variation Coefficients
Perform time-lapse analysis for individual data collected from every image
Border Contour Map
Change in area over time
Change in asymmetry over time
Change in color variation over time

## Slide 4
Perform single-image Analysis on every image
Process Overview
Prompt user to input image stack
Prompt user to crop the ruler and mole
Find the pixel/mm conversion factor
Detect the
lesion border
Calculate lesion
area
Calculate asymmetry coefficients
Calculate Color
Variation Coefficients
Data Analysis and Time-lapse
Asymmetry
Border
Color Variegation
Diameter
Evolving

## Slide 5
Input Image Stack
Images requires lesion and millimeter ruler at same focal length for pixel-mm conversion factor calculation

## Slide 6
User Input - Cropping
Ruler Crop
Mole Crop

## Slide 7
Finding the mm/pixel conversion factor (CF)
dx
dy
Notes: 𝑑= √(〖𝑑𝑥〗^2+〖𝑑𝑦〗^2 )
𝑑= √(〖𝑑𝑥〗^2+〖𝑑𝑦〗^2 )
𝐶𝐹= (1 𝑚𝑚)/(𝑑 𝑝𝑖𝑥𝑒𝑙𝑠)

## Slide 8
Detecting the lesion border
XY Coordinates for the Border
Binarized Image

## Slide 9
Calculate the lesion area
Binarized Image
Sum the number of pixels considered part of the mole
Convert the area to millimeters

## Slide 10
Calculate asymmetry coefficients
Circularity Index
A measure of how much of a perfect circle the lesion is
where
Note: If Circ > 1, the object is elliptical. If Circ < 1, the object must have fairly jagged edges.
Plane of Symmetry Testing
Rotate through θ from 0° to 179°.
Overlap the image across the line of symmetry and calculate the percent match.
Output the highest percent match as the symmetry coefficient
θ
Difference in Elliptical Perimeter
Fit the object to an ellipse based off of major and minor axes
Calculate the difference in perimeters between the two as a percentage (object perimeter as described previously). A higher percentage value means the object has more jagged edges.

## Slide 11
Calculate color Variation Coefficients
Kristen do this, idk wat it is

## Slide 12
Data Analysis and Time-lapse
Analyzing the ABCDE’s of inputted lesions
Asymmetry
Border
Color
Diameter
Evolving

## Slide 13
Asymmetry
Data Analysis and Time-lapse
Calculate “maxPercentOverlap” from plane of symmetry testing
maxPercentoverlap= 0-33.3%
maxPercentoverlap= 33.3-66.7%
maxPercentoverlap= 66.7-100%
Warning: lesion asymmetrical, highly suspicious.
Caution: lesion somewhat asymmetrical, suspicious.
Lesion symmetrical.
Output

## Slide 14
Border
Data Analysis and Time-lapse
Calculate “deltaPerimeter” from difference in elliptical perimeter testing
deltaPerimeter= 0-33.3%
deltaPerimeter= 33.3-66.7%
deltaPerimeter= 66.7-100%
Warning: lesion has ragged, irregular shape, highly suspicious.
Caution: lesion has somewhat irregular shape, suspicious.
Lesion has regular, round shape.
Output

## Slide 15
Color
Data Analysis and Time-lapse
Calculate “SSI” between lesions.
SSI= 0-33.3%
SSI= 33.3-66.7%
SSI= 66.7-100%
Warning: color variegated, highly suspicious.
Caution: color somewhat variegated, suspicious.
Color evenly distributed.
Output

## Slide 16
Diameter
Data Analysis and Time-lapse
Calculate “diameter” from major axis approximation.
Diameter= > 6mm
Diameter= 4-6mm
Diameter= < 4mm
Warning: lesion is large in diameter, highly suspicious.
Caution: lesion is somewhat large in diameter, suspicious.
Lesion has regularly sized diameter.
Output

## Slide 17
Evolving
Data Analysis and Time-lapse
Calculate “radialgrowthrate”
Radialgrowthrate > 0.13mm/month
Radialgrowthrate= 0.065-0.13mm/month
Radialgrowthrate < 0.065mm/month
Warning: lesion rapidly growing radially.
Caution: lesion slowly growing radially.
Lesion not growing radially.
Output
Calculate “verticalgrowthrate”
Verticalgrowthrate > 0.065mm/month
Verticalgrowthrate= 0.0325-0.065mm/month
Verticalgrowthrate < 0.0325mm/month
Warning: lesion rapidly growing vertically.
Caution: lesion slowly growing vertically.
Lesion not growing vertically.

## Slide 18
Characteristic | Results (Warning, Caution, or Benign) | Score
Asymmetry | Ex. Benign (94%) | 94
Border | Ex. Warning (22%) | 22
Color Variegation | Ex. Caution (63%) | 63
Diameter | Ex. Benign (3mm) | 83.3
Evolving- radially | Ex. Warning (.15mm/month) | 23.1
Evolving-vertically | Ex. Caution (.04mm/month) | 59.0
Summary | Benign- 2 Caution- 2 Warning- 2 | 57.4
Recommendation 0-25: Most likely lesion is benign. Monitor monthly. 25-50: Questionable lesion. Closely monitor biweekly. 50-75: Suspicious lesion, consult a doctor to determine if a biopsy is necessary. 75-100: Highly suspicious lesion, consult a doctor immediately about seeking a biopsy. |  | 
Summary
Notes: Diameter:
<2-4 score of 100-66.7
4-6 score of 66.7-33.3
6->8 score of 33.3-0
Score= 100-16.667*(diameter-2) (unless <2 or >8)
Evolving-radially:
0-.065 score of 100-66.7
.065-.13 score of 66.7-33.3
.13- >.195 score of 33.3-0
Score= 100-512.8205*(diameter)
Evolving-vertically:
0-.0325 score of 100-66.7
.0325-.065 score of 66.7-33.3
.065- >.0975 score of 33.3-0
Score= 100-1025.641*(diameter)

## Slide 19
Timelapse Creation:
Border Contour
Scan through lesion cropped images to find the largest image
Use CF to scale all images up to the maximum size.
Interpolate data points in between defined points created by scaling.
Plot borders on the same map as a contour map
There might be something here to make it an image???

## Slide 20
Time-lapse Creation:
Area
Image1:
Calculate lesion
area
Image 2:
Calculate lesion
area
 | Value
1 | Area
2 | Area
Create data array.
Notes: How does this fit into ABCDE?

## Slide 21
Time-lapse Creation:
Asymmetry
Calculate asymmetry coefficients

## Slide 22
Time-lapse Creation:
Color Variation
Kristen do this, idk wat it is

## Slide 23: Validation

## Slide 24: Future Directions

## Slide 25
Improve accuracy of color variegation calculation
Standardize image capture with molescope device
Integrate device with user-friendly smartphone application
Test more data sets to validate image analysis
Advertise application, find investors